Pharmaco-kinetic models
Jan Axelsson 2019-FEB-14
## Background
Imlook4d handles a number of pharmaco-kinetic models for dynamic PET scans.
Most of the models described can be calculated for a region-of-interest, or as parametric images (in which each pixel is handled as a region-of-interest). Therefore, in below descriptions, region-of-interest can be read as either region-of-interest or pixel, depending what you wish to calculate.
Models on ROIs are started from the “SCRIPTS/Model on ROIs” menu.
Models on images are started from the “MODELS” menu.
## Reference Regions
Most of the models are based on reference regions. The assumption is that a reference region very similar to the regions you want to study exists, with the only difference that an uptake mechanism (receptors or other binding) are also present.
In order to calculate a model, a reference region has to be defined.
In imlook4d, the reference region is defined as one or more region-of-interest (ROI). First ROIs are drawn, and secondly the user defines which ROIs should be used as a reference region. “Select Reference region” command can be selected from either the “SCRIPTS/Model on ROIs/Select Reference region” menu, or from “MODELS/ Select Reference region” menu. Trying to invoke a model without a defined reference region, will ask you to define it by opening the selection dialog.
## Multiple Time Graphical Analysis
Sometimes referred to as graphical methods. Turku PET centre describes this class of methods this way: In these methods, the tracer concentration curves of tissue region-of-interest and arterial plasma are transformed and combined into a single curve that approaches linearity when certain conditions are reached. The data could be plotted in a graph, and line can be fitted to the linear phase.
Examples of such methods are Logan, Zhou, and Patlak plots (see below).
These methods have in common that the start and end of the linear phase has to be defined by the user. Therefore, typically data is analyzed graphically for ROIs (menu “SCRIPTS/Model on ROIs”), and the user makes a guess of start and end frames. Inspecting the curves for the ROIs, the guess can be updated until the line fits the linear part of the curve. Typically the start frame is modified, and the end frame is the last frame of the dynamic scan.

Figure1. Left), Logan plot for one reference (ROI2) inidicated with “*”, and one region of interest (ROI1). Right) the same graph zoomed in to see that the line fits the linear phase of the curve of the region of interest.
## Receptor models (= reversible binding)
The following models are implemented both for ROIs, and for making model images (parametric images). The models calculate non-displaceable Binding Potential, BPND , which is described as a combination measure of available receptor density Bavail and affinity 1/KD. BPND = Bavail / KD. Many of the model gives additional parameters, at the cost of robustness especially for model images. Therefore, the choice of model is dependent on data quality and what parameters are of interest.
- Reference Logan. This model calculates the so called non-displaceable Binding Potential, BPND, using a reference region. For most tracers, cerebellum is devoid of receptors and used as a reference region. Calculates:
  - BPND

  Input parameters are:
  - start frame (see Multiple Time Graphical Analysis above, on how to determine start frame)
  - end frame
  - k2p transport from free to plasma, which for some tracers (for instance raclopride) can be ignored by leaving this field blank (value 0 is not allowed).
  See https://doi.org/10.1016/S0969-8051(00)00137-2
- Zhou Logan-model. This is another implementation of reference Logan, which is more robust to noise. Calculates:
  - BPND

  Input parameters are:
  - start frame (see Multiple Time Graphical Analysis above, on how to determine start frame)
  - end frame

  Zhou is preferred over Logan for model images, since it is more robust on noisy data.

  See https://doi.org/10.1016/j.neuroimage.2008.09.021
- SRTM – Simplified Reference Tissue Model, assumes, that mathematically, the kinetics of the receptor region and the region of interest is described by the same equation (kinetics not distinguishable). SRTM model calculates the following parameters:
  - BPND
  - R1 = K1/K1ref accounting for difference in delivery for region and reference region
  - k2 transport from free to plasma in region of interest
  - k2p transport from free to plasma from reference region

  in addition the following parameter, used in the calculation, is reported:
  - k2a apparent (overall) rate constant for transfer from specific compartment to plasma. This comes from the assumption of kinetics being hard to distinguish between reference region and region of interest.
  No input parameters asked for.

  See https://doi.org/10.1006/nimg.1996.0066
- SRTM2 – Two-step Simplified Reference Tissue Model. Same assumptions as in SRTM, with addition that k2p is set constant in whole brain. This model calculates the following parameters:
  - BPND
  - R1 = K1/K1ref accounting for difference in delivery to region and reference region or pixel

  Input parameter:
  - k2p from SRTM. Constant value for whole brain (or representative regions of interest), calculated using SRTM for brain outside reference region

  SRTM2 is preferred over SRTM for model images, since it is more robust.
  See https://doi.org/10.1097/01.WCB.0000033967.83623.34
  This reference describes the SRTM2 model as:
  1. Use SRTM to calculate R1, k2, and k􏰀2p for all brain voxels. Calculate a global k􏰀2p from all pixels outside the reference region.
  2. Fix k2p to the global value and calculate functional images of BP and R1 (using the SRTM2 function in imlook4d – my comment)