## Imlook4d pharmacokinetic models
Jan Axelsson 2017-MAR-09
## NEW functions
### A new framework
Path: imlook4d/MODELS/imlook4d_model/models/
- ROI-based methods (too slow for imagebased)
- TACT structure
        TACT .mean 2D matrix - ROI data in columns
        TACT .midtime 1D matrix - frame midtime in column
        TACT .duration 1D matrix - frame duration in column
        TACT .names Cell - ROI names
Uses model function that calculates the time-activity curve for given coefficients and input function
y = Logan(t,dt, Cref ,coefficients
y = srtm(t,dt, Cref , coefficients, model)
Non-linerar fits are used to find the coefficients that best describe the measured data. This is done with the helperfunction:
[TACT_out coefficients] =
regionalModel( TACT, inputFunction, modelFunction, pguess, varargin)
In addition, helper functions to transform data exists:
[TACT_out] = resample1D( TACT, method, varargin)
which can transform TACT:
create new time points
modify time scale
modify axes (to Logan)

### Functions implemented with this framework:
[R1, k2, BP] = imlook4d_srtm(TACT, refColumn, model)

## OLD functions
Image based models.

These can be tricked to be used with ROI-based by making an image with a few pixels representing the ROI values.

[outputData, X, Y] = imlook4d_logan(dataMatrix, time, duration, startFrame, endFrame, referenceData, type)

[outputData, X, Y]=imlook4d_zhou(dataMatrix, time, duration, startFrame, endFrame, referenceData, type)

outputImage=water( handles, matrix,outputFrameRange)

function [outputData, X, Y]=imlook4d_logan(dataMatrix, time, duration, startFrame, endFrame, referenceData, type)
%function outputData=imlook4d_logan(dataMatrix, time, duration, startFrame, endFrame, referenceData, type)
%
% Logan parametric image for imlook4d
%
% Input:
% dataMatrix 4D dynamic scan
% time 1D time for each frame (unit seconds)
% duration 1D duration for each frame (unit seconds)
% startFrame first frame for line fit
% endFrame last frame for line fit
% referenceData 1D time-activity data for reference data (plasma)
% type 'slope' or 'intercept'. 'slope2' for pca-based (orthogonal regression )
%
% Output:
% outputData parametric image (2D matrix)
% X optional - new X axes for each pixel (2D matrix)
% Y optional - new Y axes for each pixel (2D matrix)
%
% Jan Axelsson

function [outputData, X, Y]=imlook4d_zhou(dataMatrix, time, duration, startFrame, endFrame, referenceData, type)
%
% Zhou zhou-like parametric image for imlook4d
%
% Input:
% dataMatrix 4D dynamic scan
% time 1D time for each frame (unit seconds)
% duration 1D duration for each frame (unit seconds)
% startFrame first frame for line fit
% endFrame last frame for line fit
% referenceData 1D time-activity data for reference data (plasma)
% type 'slope' or 'intercept'. 'slope2' for pca-based (orthogonal regression )
%
% Output:
% outputData parametric image (2D matrix)
% X optional - new X axes for each pixel (2D matrix)
% Y optional - new Y axes for each pixel (2D matrix)
%
% Jan Axelsson

function [R1, k2, BP] = imlook4d_srtm(TACT, refColumn, model)
%
% srtm function for imlook4d
%
% Input:
% TACT struct containing arrays
% mean 2D matrix - ROI data in columns
% midtime 1D matrix - frame midtime in column
% duration 1D matrix - frame duration in column
% names Cell - ROI names
%
% refColumn column number for reference region
% model 'Turku', 'Lammertsma' or 'Zhou'
%
% Output:
% [R1, k2, BP] SRTM
%
% Example:
% From imlook4d menu: "SCRIPTS/ROI/ROI data to workspace"
% imlook4d_srtm(imlook4d_ROI_data, 1, 'Turku');
%
%