# Regional models
Jan Axelsson
## Intro

## Time-acitivity data
All models needs ROI time activity data, and an input function. Both these consists of data pairs (time, value). The input function may be a reference region, or processed blood input data.
A time-activity struct called Data, is described as:
Data.mean	% values in rows, one column per ROI
Data.midtime	% time point, defined as mid time of frame
Data.duration	% frame duration when applicable
Data.names	% name of each roi
Both the input function and time activity data are stored in time-activity structs.
## Resampling time-activity struct
The model function requires the ROI data and the input function are sampled at the same time points, and also often that the time unit is in minutes. The resample1D function can be used to massage time-activity structs data
Example use of resample1D:
- % change times in TACT from seconds to minutes
  TACT = resample1D( TACT, 's_to_min')
- % sample TACT to time steps of 15 seconds
  TACT = resample1D( TACT, 'evenly_distributed', 15)
- % resample TACT values to sampling times of Cblood (time-activity struct)
  TACT = resample1D( TACT, 'to_new_time', Cblood)
- % extract a subrange
  TACT_subrange = resample1D( TACT, 'sub_range',32,'end');
- % transform to Logan graphical axes
  Cref = TACT.mean(:,3); % where 3 is the ROI number for reference region
  TACT = resample1D( TACT, 'logan', Cref, k2 );

## Model description
A model is described by its coefficients (could be BP, DVR, K1, k2 etc) and optional parameters describing the model.
coefficients	% array with one row, coefficients in columns
varargin	% optional parameters, depending on model
## Model function
The model function calculates model values using input time points data and coefficients. The input data needed is time t, frame duration dt, and input function at these data points. The output is put in a vector y with same dimension as t. Example of the defininition of a model function using reference data as input function:
function y = srtm(t, dt, Cref,coefficients, varargin)

- Cref is the input function, with one column of data sampled at time points t.
  Cref = TACT.mean(:, col); % col is column number for the reference ROI
- coefficients is the model description
- y is the calculated time-activity curve using the coefficients and input function.
## Solving model
Finding a model is the calculation of the model coefficients. These coefficients are determined by non-linear regression, findning the coefficients to the model function that describes the measured time-activity data the best. In this regression, the model function is passed as a function handle, for instance @srtm.
function [TACT_out coefficients] = …
regionalModel( TACT, inputFunction, modelfunction, pguess, varargin)